## Slide 1: Thermal Systems Heat Exchanger Design Presentation
Group 1
Diana Tiburcio, Jakob Werle, Yireh Byas, Selinez Soto

## Slide 2: Table of Contents
Calculations
Prototype
Fabrication
Testing
Results

## Slide 3: Problem
Design concentric tube heat exchanger
  Create largest temperature difference
  Analyze how parameters affect design choices
Constraints
  Must fit on test bench
  Cold flow temp – cold hose water
  Hot water temp – small tank w/ water heater < 100°C
Notes: JW

## Slide 4: Prototyping

## Slide 5: Calculations and Methods
Cold Constants:
  Cold flow rate: m = 0.8 L/s
  Cold temperature: T_c = 19 ℃
  k = 0.6014 W/m*K
  Pr = 7.1558
  = 4182.7 kJ/kg*K
  μ = 0.00103 Ns/m^2
  ρ = 998.0 kg/m^3
Hot Constants:
  Hot flow rate: m = 0.1 L/s
  Hot temperature: T_c = 65 ℃
  k = 0.6585 W/m*K
  Pr = 2.7414
  = 4187.3 kJ/kg*K
  μ = 0.000432 Ns/m^2
  ρ = 979.5 kg/m^3
Schematic 1: Cross sectional view of the heat exchange system
Notes: YB

## Slide 6: Calculations and Methods
= 0.2015 m/s
= 1.607 m/s
= 1,1598.0
= 2,6007.3
= 0.0297
= 0.0243
= 61.97
= 187.47
= 6,764.3
= 1,606.6
Notes: DT

## Slide 7: Calculations and Methods
U = 1,177.3
= 3,346.2
= 418.7
= 0.1251
NTU = 0.3646
Schematic 2: Detailed cross section view of the heat exchange system
Notes: DT

## Slide 8: Calculations and Methods
Parallel Flow:
Hot Output Temperature = 51.24 °C
Cold Output Temperature = 20.72 °C
Counter Flow:
Hot Output Temperature = 51.18 °C
Cold Output Temperature = 20.73 °C
= 19,261
= 5,760.5
= 5,786.7
= 0.2991
= 0.3004
Notes: YB

## Slide 9: Thermal and Flow Entrance Length
- & >> 2,300, therefore both are in turbulent flow conditions
Notes: DT

## Slide 10: Pressure Difference and Head Loss
Hot (57”)
Cold (8”)
Ball
Ball
Ball
90̊ & Contraction
90̊ & Expansion
Cold (39”)
Schematic 3: Cross sectional view of the final heat exchange system with outlined head loss and water flow
Notes: DT

## Slide 11: Design Optimization
Chart: Temperature Outputs vs. Length
| 0.2 | 0.4 | 0.6 | 0.8 | 1
Hot - Counter | 62.6275 | 59.5145 | 56.5299 | 53.7505 | 51.1803
Cold - Counter | 19.2969 | 19.6864 | 20.0599 | 20.4077 | 20.7293
Chart: Output Temperatures at Varying Cold Flowrates
| 0.2 | 0.4 | 0.6 | 0.8 | 1 | 1.2
Parallel Hot Output | 55.3521 | 52.9517 | 51.8714 | 51.2429 | 50.8274 | 50.5306
Parallel Cold Output | 23.8292 | 22.0154 | 21.1905 | 20.7215 | 20.4188 | 20.2071
Counter Hot Output | 55.2666 | 52.8679 | 51.799 | 51.1803 | 50.7726 | 50.482
Counter Cold Output | 23.872 | 22.0363 | 21.2026 | 20.7293 | 20.4243 | 20.2112
Chart: Output Temperatures at Varying Hot Flowrates
| 0.1 | 0.3 | 0.5 | 0.7 | 0.9 | 1
Parallel Hot Output | 51.2429 | 56.2704 | 58.4804 | 59.7634 | 60.6114 | 60.9374
Parallel Cold Output | 20.7215 | 22.2772 | 23.0792 | 23.587 | 23.9425 | 24.0838
Counter Hot Output | 51.1803 | 56.2246 | 58.4493 | 59.741 | 60.5946 | 60.9226
Counter Cold Output | 20.7293 | 22.2943 | 23.0986 | 23.6066 | 23.9614 | 24.1023
Figure 1: Theoretical hot and cold output temperatures of both counter and parallel flows with varying cold flowrates
Figure 2: Theoretical hot and cold output temperatures of both counter and parallel flows with varying hot flowrates
Figure 3: Theoretical hot and cold output temperatures for the counter flow heat exchanger at different lengths
Notes: DT

## Slide 12: SolidWorks Simulation

## Slide 13: Final Design
Schematic 4: Isometric view of final heat exchanger prototype

## Slide 14: Final Design
Schematic 5: Drawing and dimensions of final heat exchanger prototype

## Slide 15: Fabrication
Notes: JW

## Slide 16: Fabrication Process
Model & draw heat exchanger components in SolidWorks
Create bill of materials --> place part orders
Manufacture in house parts
Assemble & solder heat exchanger components
Leakage tests on heat exchanger
Notes: JW

## Slide 17: Bill of Materials
ITEM NO | MFR NO | DESCRIPTION | QTY | COST | NOTES
1 | 5175K136 | Cu Pipe 1.125 OD x 1.055 ID x 57 L | 57 | $0.53 | Provided by COE
2 | 5175K136 | Cu Pipe 1.125 OD x 1.055 ID x 2 L | 2 | $0.53 | Provided by COE
3 | 5175K138 | Cu Pipe 1.625 OD x 1.527 ID x 39 L | 39 | $1.08 | Provided by COE
4 | 5175K138 | Cu Pipe 1.625 OD x 1.527 ID x 8 L | 8 | $1.08 | Provided by COE
5 | - | Backing Board | 1 | - | Provided by COE
6 | - | 3D Print Brackets | 4 | - | 3D Printed in COE
7 | 5520K215 | Solder-Connect Fitting for Copper Tubing (Tee) | 2 | $19.30 | Right-Angle Tee, Female Socket-Connect, 1-1/2 x 1 Tube Size
8 | 5520K411 | Solder-Connect Fitting for Copper Tubing (Adaptor) | 4 | $9.30 | Adapter, Female Socket-Connect, 1 Tube Size x 3/4 NPT Female
9 | 47865K55 | Brass On/Off Valve | 3 | $28.41 | Solder-Connect Female for 1-1/8" Tube OD
10 | 8624K44 | Moisture-Resistant HDPE Rod 2-1/2 OD x 24 L | 1 | $74.50 | Makes 8 pieces
11 | 5350K31 | Zinc-Plated Steel Barbed Hose Fitting | 4 | $4.86 | For Air and Water, Adapter for 1/4" Hose ID, 1/8 NPT Male
 |  |  | TOTAL | $336.93 | 
 |  |  | ACT | $227.71 | 
Figure 4: Chart of All Components of the Heat Exchanger System with Corresponding Costs
Notes: JW

## Slide 18: Overall Assembly
Schematic 6: Blown up view of part assembly for final heat exchanger prototype
Notes: JW

## Slide 19: Sensor Mounting
Material: High Density Polyurethane ~0.4 W/m*K
HDPE chosen to isolate thermocouples from adjacent heat transfer
Sized so probe sits in stream, not to interrupt flow
Press fit onto copper tubing
Leak tested separately
Image1: 3D Schematic and actual view of sensor mounting
Notes: JW

## Slide 20: Tubing Prep and Assembly
Tubing cut with pipe cutter
Dry fitment
Prepare connections
  Scuff tubing
  Flux
Solder 1st set connections
Press sensor collars
Solder 2nd set connections
Image 2: Solder and Press sensor Assembly
Notes: JW

## Slide 21: Fabrication Re-considerations
NPT threading wears out in HDPE – different material or mounting style
Low tolerance copper tubing not adequate for press fit
Longer barbs for pressure lines
Ball valve leakage – likely from over heating of seal during soldering
Design thermocouple connector manifold – take readings more efficiently
Notes: JW

## Slide 22: Testing

## Slide 23: Testing Apparatus
Image 3: Complete view of testing apparatus and set up in parallel flow
Notes: Selinez

## Slide 24: Testing Procedure
Allow hot water tank to heat to ~65°C (3+ hrs)
Install thermocouples and attach pressure lines
Attach water lines to heat exchanger – configure parallel or counter flow
Open cold water spicket and turn on hot water pump
Adjust flow rates to trial specification
Allow temperatures to stabilize then read 3x per trial:
  Inlet hot & cold temperatures
  Outlet hot & cold temperatures
  Pressure differential hot & cold
Allow hot water tank to reheat in between trials (~15min)
Notes: Selinez

## Slide 25: Testing Example
Video 1: Running experimental trials for counterflow flow rates

## Slide 26: Testing Complications
Thermocouple failure and calibration errors
  Rebuild attempted
  Offset values
Cavitation in hot flow
  Pressure reading inaccuracies
Small leaks from NPT threads
Plastic tubing failure
Image 4: Rebuilt thermal couple and attached pressure tube
Notes: JW

## Slide 27: Results

## Slide 28
 |  |  | Hot Side Flow Rate (L/min) | Cold Side Flow Rate (L/min) | Cold Inlet Temp | Cold Outlet Temp | Bath Temp | Hot Inlet Temp | Hot Outlet Temp
Target Cold Flow Rate (L/min) | 0.8 | Experimental Trial 1 | 6.45 | 48.2 | 12.2 | 13.2 | 65 | 47.1 | 36.6
Target Hot Flow Rate (L/min) | 0.1 | Experimental Trial 2 | 6.5 | 47.9 | 12.1 | 13.2 | 67 | 41.5 | 36.7
 |  | Experimental Trial 3 | 6.5 | 48.1 | 10.9 | 12.4 | 66 | 60.3 | 37.45
 |  | Average | 6.48 | 48.07 | 11.73 | 12.93 | 66.00 | 49.63 | 36.92
 |  | Temperature Change |  |  | 1.20 |  |  | 12.72 | 
Target Cold Flow Rate (L/min) | 0.8 | Experimental Trial 1 | 12.1 | 48 | 12.2 | 14.3 | 65.6 | 59.6 | 43.3
Target Hot Flow Rate (L/min) | 0.2 | Experimental Trial 2 | 12.4 | 48.2 | 11.5 | 13.45 | 66 | 59.5 | 38.6
 |  | Experimental Trial 3 | 12.6 | 48.1 | 12.4 | 14.4 | 66 | 60.5 | 38.8
 |  | Average | 12.37 | 48.10 | 12.03 | 14.05 | 65.87 | 59.87 | 40.23
 |  | Temperature Change |  |  | 2.02 |  |  | 19.63 | 
Target Cold Flow Rate (L/min) | 0.8 | Experimental Trial 1 | 48.4 | 48.3 | 12.2 | 18.9 | 67.3 | 58.1 | 52.1
Target Hot Flow Rate (L/min) | 0.8 | Experimental Trial 2 | 48.4 | 48.1 | 11 | 19.3 | 65 | 62.5 | 55.2
 |  | Experimental Trial 3 | 48 | 48.1 | 11.7 | 18 | 66.3 | 63.1 | 56.5
 |  | Average | 48.27 | 48.17 | 11.63 | 18.73 | 66.20 | 61.23 | 54.60
 |  | Temperature Change |  |  | 7.10 |  |  | 6.63 | 
Parallel Flow Experimental Results
Figure 5: Experimental results of the parallel flow heat exchanger tests at different flow rates
Notes: DT

## Slide 29
 |  |  | Hot Side Flow Rate (L/min) | Cold Side Flow Rate (L/min) | Cold Inlet Temp | Cold Outlet Temp | Bath Temp | Hot Inlet Temp | Hot Outlet Temp
Target Cold Flow Rate (L/min) | 0.8 | Experimental Trial 1 | 6 | 48.6 | 10.1 | 11.7 | 66.3 | 64.3 | 48
Target Hot Flow Rate (L/min) | 0.1 | Experimental Trial 2 | 5.9 | 48.2 | 9.9 | 11.6 | 66 | 65.05 | 48.45
 |  | Experimental Trial 3 | 6 | 48.7 | 10.1 | 11.6 | 66.4 | 65.4 | 48.2
 |  | Average | 5.97 | 48.50 | 10.03 | 11.63 | 66.23 | 64.92 | 48.22
 |  | Temperature Change |  |  | 1.60 |  |  | 16.70 | 
Target Cold Flow Rate (L/min) | 0.8 | Experimental Trial 1 | 12.4 | 48.2 | 10.55 | 12.45 | 66.75 | 62.4 | 56.3
Target Hot Flow Rate (L/min) | 0.2 | Experimental Trial 2 | 12.4 | 48.2 | 10.1 | 12.3 | 66 | 64.9 | 55.5
 |  | Experimental Trial 3 | 12.4 | 48.2 | 9.9 | 12.2 | 66 | 64.8 | 55.8
 |  | Average | 12.40 | 48.20 | 10.18 | 12.32 | 66.25 | 64.03 | 55.87
 |  | Temperature Change |  |  | 2.13 |  |  | 8.17 | 
Target Cold Flow Rate (L/min) | 0.5 | Experimental Trial 1 | 6.3 | 30.25 | 10 | 12.3 | 66 | 65 | 49.6
Target Hot Flow Rate (L/min) | 0.1 | Experimental Trial 2 | 6.3 | 30.1 | 10.2 | 12.5 | 66.75 | 65.55 | 50
 |  | Experimental Trial 3 | 6.3 | 30.1 | 10.1 | 12.9 | 66.7 | 65.2 | 49.8
 |  | Average | 6.30 | 30.15 | 10.1 | 12.57 | 66.48 | 65.25 | 49.8
 |  | Temperature Change |  |  | 2.47 |  |  | 15.45 | 
Counter Flow Experimental Results
Figure 6: Experimental results of the counter flow heat exchanger tests at different flow rates
Notes: YB

## Slide 30: Summary of Data – Parallel Flow
 |  |  | Theoretical |  | Solidworks |  | Experimental |  | Theoretical |  | Solidworks | 
Hot Flow Rate (L/min) | Cold Flow Rate (L/min) | Heat Transfer Rate | Hot Outlet Temp | Cold Outlet Temp | Hot Outlet Temp | Cold Outlet Temp | Hot Outlet Temp | Cold Outlet Temp | Hot Outlet Temp | Cold Outlet Temp | Hot Outlet Temp | Cold Outlet Temp
0.10 | 0.80 | 5838.35 | 50.17 | 13.86 | 53.78 | 11.66 | 36.92 | 12.93 | 26% | 7% | 31% | 11%
0.20 | 0.80 | 9059.55 | 53.60 | 15.19 | 46.42 | 12.58 | 40.23 | 14.05 | 25% | 7% | 13% | 12%
0.80 | 0.80 | 16393.81 | 56.32 | 16.54 | 56.6176 | 15.4717 | 54.60 | 18.73 | 3% | 13% | 4% | 21%
Figure 7: Comparison of the theoretical and SolidWorks results to the experimental results with corresponding percent errors.
Notes: DT SS

## Slide 31: Summary of Data - Counter Flow
 |  |  | Theoretical |  | Solidworks |  | Experimental |  | Theoretical |  | Solidworks | 
Hot Flow Rate (L/min) | Cold Flow Rate (L/min) | Heat Transfer Rate | Hot Outlet Temp | Cold Outlet Temp | Hot Outlet Temp | Cold Outlet Temp | Hot Outlet Temp | Cold Outlet Temp | Hot Outlet Temp | Cold Outlet Temp | Hot Outlet Temp | Cold Outlet Temp
0.10 | 0.80 | 5838.35 | 48.55 | 12.04 | 45.08 | 11.69 | 48.22 | 11.63 | 1% | 3% | 7% | 1%
0.20 | 0.80 | 9059.55 | 51.94 | 13.29 | 55.31 | 12.75 | 55.87 | 12.32 | 8% | 7% | 1% | 3%
0.10 | 0.50 | 5390.27 | 50.62 | 13.15 | 49.36 | 13.42 | 49.80 | 12.57 | 2% | 4% | 1% | 6%
Figure 8: Comparison of the theoretical and SolidWorks results to the experimental results with corresponding percent errors.
Notes: SS

## Slide 32: Summary of Data
Figure 9: Visual comparison of the theoretical and SolidWorks results to the experimental results.
Notes: Selinez

## Slide 33: Project Improvements
Outline project goals and constraints
Experiment run through before theory review – understand data collection
More organized testing schedule for teams
Better management of sensitive sensors – per team?
More focus on teamwork
Notes: YB

## Slide 34: Questions?