## Slide 1: Introduction to FSAE driving
TEMPLE FORMULA RACING – DRIVER CLINIC 1
Jakob Werle

## Slide 2: Jakob – who am i?
Joined TFR in 2018
  Prior suspension lead and president
  Test driver
  Pitt Shootout 17th overall
  14th place endurance co-driver
FSAE
  Technical Scrutineer (FSAE & SCCA)
  Testing pad advisor
SCCA/PCA autocross
1000+ hrs sim experience
Currently junior race engineer for ADSA Wright Racing & ANZE

## Slide 3: FSAE competition

## Slide 4: Driving Fundamentals
Vehicle Operation
Safety / equipment / environment
Controls familiarity
Starting / stopping
Shifting
Steering
Communication
Racing skills
Vision
Line choice
Efficient piloting
Driver feedback
Mindset

## Slide 5: Vehicle operations
The part that isn’t racing… yet

## Slide 6: Safety
Driver’s responsibility once car is live
Equipment
  Brakes!!!
  Harness
  Helmet
  Fire gear / fire bottles
Environment
  Awareness
  Track workers
  Track layout / obstacles
  Weather

## Slide 7: Cockpit controls
Shifter
E-stop
Ignition
Accessory
switches
Steering wheel
Tachometer / dash

## Slide 8: footbox controls
Throttle
Clutch
Brake

## Slide 9: Harness
All belts should be TIGHT and flat
A well secured driver is a safe and fast driver
Twist the quick connect to unbuckle
  (Tension will pop belts out of way for egress)
  Hip belts
    Position over hips, NOT thighs or waist
    Set lengths so QC sits in middle
  Anti-submarine belts
    Set length so QC sits just ~ 2in below belly button
  Shoulder belts
    Deep breath out
Anti-sub belt
Shoulder belt
Hip belt
Quick connect

## Slide 10: Turning car on / off
Master ground
  Connects main power
E-stop
  Press to stop engine and in emergencies
  Turns on all electronics
  Listen/look for power (fuel priming, dash lights, etc.)
Ignition
  Starts engine by cranking starter motor
  Large energy draw
  Hold for 2-3 seconds
Off
On

## Slide 11: Braking
Race car brakes
  No ABS – easy to lock up
  High pressure
  Very sensitive
Use brakes to slow down!
First line of safety for driver, crew, and track workers
In event of crisis, resort to brakes
Brake Overtravel Switch
  Kills engine when hit
  If brakes fails, pedal will move excessively

## Slide 12: Clutch
Engine RPM
Wheel RPM
=
Moving Speed
more
less
Clutch allows engine to gently provide power to wheels
  Modulate in friction zone
  Engine stalled  let out clutch too abruptly
  Fully release clutch once sufficiently moving
Just enough throttle
Release brake when ready to move
When should you clutch?
  Start moving
  Stopping
  Learning to shift

## Slide 13: Shifting
Let off throttle
Push in clutch
Shift gear
  Down shift – rev match
6 gears
Higher gears
  Faster speed range
  Typically smoother
Lower gears
  Lower speed range
  More torque / jerky
Shift when car stops accelerating
Up
Down
Neutral
(1/2 from 1st or 2nd)

## Slide 14: Racing skills
To drive slowly… the least amount of time

## Slide 15: Spatial awareness
https://www.youtube.com/watch?v=fnRwkdseC1Y

## Slide 16: Spatial awareness

## Slide 17: Spatial awareness
Hairpin
Road surface change
Vision – UP!

## Slide 18: efficient piloting
Slow is smooth… smooth is fast
  Balanced car is #1 priority
  Every input unsettles car
  Allow vehicle to work effectively
Tactics
  Gently grip – sensitive
  Smooth inputs
  Line choice – larger turns are easier for car

## Slide 19: Feedback
Consistency!
Break down sensations
  Laps
    Turns
      Entry  Apex  Exit
Think: input = output
Quality of driver’s feedback directly effects quality of setups
Setup / debrief sheets

## Slide 20: Mindset – be a champion
Racing is CHALLENGING
  Try to go in feeling good
  Stop if frustration sets in
Warm up
  Take it slow
  Build mental map
Improvement is not guaranteed
Have fun and be safe