## Slide 1: Introduction to FSAE driving
TEMPLE FORMULA RACING – DRIVER CLINIC 1
Jakob Werle

## Slide 2: Jakob – who am i?
Joined TFR in 2018
  Prior suspension lead and president
  Test driver
  Pitt Shootout 17th overall
  14th place endurance co-driver
FSAE
  Technical Scrutineer (FSAE & SCCA)
  Testing pad advisor
SCCA/PCA autocross
1000+ hrs sim experience
Currently junior race engineer for ADSA Wright Racing & ANZE

## Slide 3: FSAE competition

## Slide 4: Driving Fundamentals
Vehicle Operation
Safety / equipment / environment
Controls familiarity
Starting / stopping
Shifting
Steering
Communication
Racing skills
Vision
Line choice
Efficient piloting
Driver feedback
Mindset

## Slide 5: Vehicle operations
The part that isn’t racing… yet

## Slide 6: Safety
Driver’s responsibility once car is live
Equipment
  Brakes!!!
  Harness
  Helmet
  Fire gear / fire bottles
Environment
  Awareness
  Track workers
  Track layout / obstacles
  Weather

## Slide 7: Cockpit controls
Shifter
E-stop
Ignition
Accessory
switches
Steering wheel
Tachometer / dash

## Slide 8: footbox controls
Throttle
Clutch
Brake

## Slide 9: Harness
All belts should be TIGHT and flat
A well secured driver is a safe and fast driver
Twist the quick connect to unbuckle
  (Tension will pop belts out of way for egress)
  Hip belts
    Position over hips, NOT thighs or waist
    Tighten across body
  Anti-submarine belts
    Set length so QC sits just ~ 2in below belly button
  Shoulder belts
    Deep breath out
Anti-sub belt
Shoulder belt
Hip belt
Quick connect

## Slide 10: Braking
Race car brakes
  No ABS – easy to lock up
  High pressure
  Very sensitive
Use brakes to slow down!
First line of safety for driver, crew, and track workers
In event of crisis, resort to brakes
Brake Overtravel Switch
  Kills engine when hit
  If brakes fails, pedal will move excessively

## Slide 11: Clutch
Engine RPM
Wheel RPM
=
Moving Speed
more
less
Clutch allows engine to gently provide power to wheels
  Modulate in friction zone
  Engine stalled  let out clutch too abruptly
  Fully release clutch once sufficiently moving
Just enough throttle
Release brake when ready to move
When should you clutch?
  Start moving
  Stopping
  Learning to shift

## Slide 12: Shifting
Let off throttle
Push in clutch
Shift gear
  Down shift – rev match
6 gears
Higher gears
  Faster speed range
  Typically smoother
Lower gears
  Lower speed range
  More torque / jerky
Shift when car stops accelerating
Up
Down
Neutral
(1/2 from 1st or 2nd)

## Slide 13: Racing skills
To drive slowly… the least amount of time